# WBTV 1 : Publish-Subscribe for Embedded Devices
## Introduction
This page presents a simple protocol for realizing publish-subscribe messaging in small low cost embedded devices using ordinary UART(8-n-1) over any wired-AND physical layer.
The protocol can be implemented in about 3K of memory+ 70 bytes of RAM.
The protocol has no special dependence on timing of byte arrivals and does not rely on timeouts to detect a node that has failed during transmission.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## Semantics
Each message can be thought of as pushing a “message” made of “segments” to a “channel”. Both the message segments and the name of the channel are arbitrary 8 bit strings.
All channels with <6 byte names are reserved for future standardization.
To avoid conflicts, channel names should be based on URLs or UUIDs or some other unique string, but can simply be chosen arbitrarily when global compatibility is not required.
Channels can be thought of as inputs or outputs or both of the node that “owns” the channel.
Devices can use a common prefix for all their owned channels but are not required to.

## Message Structure
Every message begins with an exclamation point, followed by the N byte channel name, then a tilde as a separator , then the data, then a 2 byte checksum, then a closing newline(ASCII 10). All data should always be little-endian.
Should the message contain multiple segments, separate them with un-escaped tildes.
## Escaping
Should a control symbol(!, ~, or \n) need to appear in data or channel name, the backslash is used to escape it. The character following a non-escaped backslash(even another backslash) is processed as a literal character.
## Checksum
The checksum is a fletcher-256 sum, as defined by the following function :
set fast and slow to zero
then for each byte to be hashed:
increment slow by the byte mod 256
increment fast by slow mod 256

Calculated over all the bytes of the raw channel, the tilde, and the raw message, but not including the escapes or any other control characters except for the tilde. The checksum is appended to the message slow byte first, making the full message structure:
!<channel>~<message><fast><slow>\n
## CSMA
To remove the need for a bus master, we use the wired-OR Physical Layer and CSMA/CD. Before sending a message, a device must pick a random length of time, and wait until the bus has been free for that time.
Devices must also listen while transmitting, and, if they detect a collision(via the wired-or), immediately cease, wait another random period(preferably 2x the initial period) and retry.
# WBTV Reserved Channel Assignments
## Introduction
This document defines several standard channels for use with WBTV. Where legally possible, I release this document to the Public Domain. Elsewhere I license it under the Creative Commons Zero license.
## Channels
The following channels are defined;
### ASK
Used to request transmission of a message of a particular channel. The data should be the channel name. No device is required to respond.
### TIME
Any device may send on this channel. The data must be a 64 bit number containing the number of seconds since the POSIX epoch, ignoring leap seconds(i.e. A posix timestamp), followed by a 16 bit number containing the milliseconds part. After this may be a single 8 bit signed integer containing the binary logarithm of the estimated accuracy in seconds.
### Single Letter Channels
All channels whose name is a single printable ASCII character are reserved for manual assignment, whether by DIP switch, through software, through hardcoding, or any other method.