# WBTV 2: Time Synchronization Protocol
Version 1 By Daniel Dunn
# WBTV 3: Device Discovery and ID
Version 1 by Daniel Dunn
# WBTV 4: Service Discovery
Version 1 by Daniel Dunn, Public Domain/CC0
# WBTV 5: The DAQ Service
Version 1 by Daniel Dunn
# WBTV 6: DAQ Service Extensions
Version 1 by Daniel Dunn
# WBTV 9: Misc
Version 1 by Daniel Dunn, Public Domain/CC0
# WBTV 10: Physical Layer
Version 1 by Daniel Dunn, Public Domain/CC0
# WBTV 11: Nick IDs
Version 1.1 by Daniel Dunn, Public Domain/CC0
# WBTV 12: Navigation Device Protocol
Version 1 by Daniel Dunn, Public Domain/CC0
# WBTV 8: Stage Light Control Extensions
Version 1 by Daniel Dunn, Public Domain/CC0
# WBTV 13: Stage Info Protocol
Version 1 by Daniel Dunn, Public Domain/CC0
# WBTV 14: Format Specifier Bytes
Version 1 by Daniel Dunn, Public Domain/CC0
# WBTV 15: IO Protocol
Version 1 by Daniel Dunn, Public Domain/CC0
# WBTV 16: IO Protocol Classes
Version 1 by Daniel Dunn, Public Domain/CC0
## Introduction
# WBTV 1 : Publish-Subscribe for Embedded Devices
Revision 1 by Daniel Dunn, Public Domain CC0
This page presents a simple protocol for realizing publish-subscribe messaging in small low cost embedded devices that can be realized without special hardware over a variety of interfaces, including USB and 8-N-1 UART.

The protocol can be implemented in about 3K of memory+ 70 bytes of RAM.

Implementation of a one-to-one topology only requires a channel through which bytes can be sent. Implementing a bus topology requires a medium supporting collision detection, which can be as simple as an I2C/TWI-Like interface and standard UART.
## Semantics
Each message can be thought of as pushing a “message” made of “segments” to a “channel”. Both the message segments and the name of the channel are arbitrary 8 bit strings.

All channels with <=6 byte names are reserved for future standardization.

To avoid conflicts, channel names should be based on URLs or UUIDs or some other unique string, but can simply be chosen arbitrarily when global compatibility is not required.

## Message Structure
Every message begins with an exclamation point, followed by the N byte channel name, then a tilde as a separator , then the data, then a 2 byte checksum, then a closing newline(ASCII 10).

Should the message contain multiple segments, separate them with un-escaped tildes.

All data sent over WBTV should always be little-endian unless there is a special reason to prefer otherwise. There is no hard limit to the message length, but messages should be kept as short as possible.

## Escaping
Should a control symbol(!, ~, or \n) need to appear in data or channel name, the backslash is used to escape it. The character following a non-escaped backslash(even another backslash) is processed as a literal character.
## Checksum
The checksum is a fletcher-256 sum, as defined by the following function :
set fast and slow to zero
then for each byte to be hashed:
increment slow by the byte mod 256
increment fast by slow mod 256

The function is calculated over all the bytes of the raw channel, the tildes betweeen segments, and the raw message, but not including the escapes or any other control characters except for the tilde.

The checksum is appended to the message slow byte first, making the full message structure(control chars underlined):
!<channel>~<message><fast><slow>\n
## CSMA
When using a bus topology, a device must listen before transmitting to ensure the bus is free. With 8-N-1 UART, the bus can be considered free if it has been continually in the idle state for 1.5 Byte-Times.

If the bus is found to not be free, devices must wait a random period before sensing the bus again.

Devices must also listen while transmitting, and, if they detect a collision(via the wired-or), immediately cease, wait a random period, and retry, repeating as necessary, preferably with an exponentially increasing random period.

0 to 3 byte times is the suggested default range for initial random delays and for waiting to sense the bus again.

To catch collisions early without wasting time, a random delay of 0 to 2 bit-times can be inserted between bytes of the header.

## Introduction
Often there is a need to provide accurate time synchronization to many devices. This document defines a reserved channel for that purpose.

## The TIME Channel
The TIME channel is reserved for broadcasting messages that represent the current time, as of the leading edge of the start bit of the initial ! In the message. Messages must be timestamps conforming to the following format.
## Time Stamp Format
A time stamp contains the following fields, concatenated together, plus any optional fields which may be added, which may be specified in a later document.
### UNIX Time Stamp
This must be a 64-bit signed integer representing the number of seconds elapsed since 00:00 1 January 1970, excluding leap seconds. This is identical to the 64 bit UNIX time number.
This gives enough precision for all of recorded history until millions of years from now.
### Fractional Part
This is a 32 bit unsigned integer representing the fractional part of the current time multiplied by 2**32. Where the fractional part is unknown, 2**16 should be sent to minimize average error.
### Accuracy Estimate
This is an estimate of the accuracy, given as a 8 bit signed integer E followed by am 8 bit unsigned integer M, where the maximum error in seconds is M*(2^E).

This is an extremely simple floating point format that can only represent positive integers.

The estimate should be conservative, and should be the maximum error the sender is rated to experience across the full range of working conditions.
## Device Behavior
Devices should avoid sending time messages during leap seconds, as the time number is ambiguous. Devices should be able to be configured to send time data rather frequently, on the order of up to every several seconds, to account for devices without accurate clocks.

Devices should maintain an estimate of error for their internal clock, and should ignore messages that advertise more error than that, i.e. devices with an accurate estimate of the time should ignore broadcasts from devices with a less accurate estimate of the time.

Devices should not ideally send the time if a time message with equal or better accuracy has been recently sent, specifically, if a receiver with a 2% accurate clock would not have accumulated more error than the internal estimate, there is likely no use in sending the time.

## Introduction
Often it becomes necessary to uniquely identify a device, and to enumerate devices on the bus. This document establishes rules for device IDs for WBTV devices.
## The Device UUID
Every device should, but is not required to, have a 16 byte UUID, which may conform to an official UUID standard of may simply be a random string. A devices UUID should never change, and no two devices should ever have the same UUID. Big-endian encoding should be used for all UUIDs used with the WBTV protocol, even though WBTV is normally little-endian.

## Friendly Name
Devices should, but are not required to, be able to accept a user-assigned friendly name. The method of assigning a name should be to send a single packet to channel NAME containing the target device ID followed by the name, then the end of packet.
Names may not be longer than 24 characters, and must be valid UTF-8.
Devices should announce their names at power-up or on connection, by sending their device UUID followed by their name to the MYNAME channel.
## The STATUS channel
The channel STATUS is reserved for devices to post short status updates. Messages must be composed of the device's UUID, then optionally a newline and a set of space separated keywords, then by a newline and free text.
Device specific Keywords should begin with “x-”.
General Keywords:

power-warn	Low input voltage
power-fail	Insufficient input power
temp-warn	Overtemperature warning
temp-fault	Overtemperature fault
volt-warn	Overvoltage warning
normal	Normal Operation

Most devices should not send STATUS messages, however for some devices a heartbeat/still connected signal is important.
## The INFO channel
This channel is used by devices to transmit information about themselves to the network.
Messages must be composed of the device's UUID followed by a newline, followed by the manufacturer name, another newline, the
product name, another newline, then two newlines and any amount of free description.
## The SCAN channel
Posting a message to the SCAN channel allows one to scan the network for devices. All devices receiving a blank message on this channel should send any information they may have about themselves and channels they own to the network.
Devices should NOT immediately send their info, but should wait a random time from 0 to 20s or so, during which time they should continue normal operation. Devices should only use SCAN with full knowledge that the network may be heavily trafficked from responses.

## Introduction
Automatic network configuration is a common requirement. Consider a wind speed sensor that sends data on a specific channel, which obviously must be different between devices to allow for multiple devices to be used. How can we know what channel a device sends on?

This document defines the concept of a WBTV Service. A WBTV Service is simply a type of service a device can provide on a channel. The wind speed sensor could be thought of as providing a “wind speed service” on the channel it sends on, and a light controller could be thought of as providing a “Light Control Service” on the channel that it listens on.

Services are identified using UUIDs, and as such anyone can define a service, and publish it formally or informally in the appropriate manner, such as online or in a user manual.

Devices that provide services must have a unique UUID that is not shared even between identical devices. This UUID may also be used as a channel name without conflict to save ram.

There is no restriction against two compatible services sharing a channel.

## The SERV Channel
The SERV channel is reserved for service announcements, which should be made after a device powers up, or in response to SCAN messages. and messages must obey the following format:

### Owning Device
The first 16 bytes of a SERV message must contain the UUID of the owning device which is providing the advertised service.
### Service UUID
The next 16 Bytes must be the UUID of the service being provided.

### Channel Len
The length of the channel name of the channel on which thee service is provided in bytes, represented as one byte.
### Channel
The channel name on which the service is provided.
### Modifier Bytes
Any further data is to be interpreted in a service- and device specific manner.
## The Null Service
This is a service with a UUID of 16 zeros. It has no specific definition. One must use the modifier bytes and device documentation to explain the channel.
## The Struct Service
This service is used for simple sensors and the like. The modifier bytes must be C source code containing either or both of two struct definitions, one called input and the other output. Data sent to the device must be an unpadded packed little endian instance of input. And data sent from the device must match output.

## WBTV-DAQ Service
This is a WBTV4 Service that allows a device to act as a data acquisition device.

Service UUID(hex): 0x8A9E60340D8611E4843156F31D5D46B0
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## Modifier Bytes
The modifier bytes are to be used to define a set of signals, wherein each line defines a signal(the first line defining signal 0) and so on.
Signals 128+ are reserved, with signal 128 representing a UNIX timestamp, consisting of a 16 bit seconds part and 16 bit fractional part,
This will roll over every 2^16 seconds, which is not an issue because arrival time can be used to disambiguate.
Each line is to consist of, at minimum, a type and a name(which may not include spaces), as in the example:
## u16 Position
Which would represent a signal called position, which is represented as a 16 bit unsigned integer.
### Valid Types
The types that are defined in this document are:
#### u8, u16, u32, u64, u128
Unsigned integer of specified bit width
#### i8, i16, i32, i64, i128
Signed integer of specified bit width.
#### f16, f32, f64, f128
IEEE Float of specified bit width.

### Keywords
The name and type may optionally be followed by any number of keywords, some of which may have arguments, That may appear in any order.
#### in <unit>
Specifies a unit or interpretation to be used with the channel. <unit> must not contain any spaces, and should where possible be an SI base or derived unit, with ^ used to denote exponentiation where needed e.g. for “mW/cm^2” Example:
## u16 speed in mm/s
#### range <min>:<max>
Applies to numeric types. Specifies that the number reported for this signal will be in the specified range. Expressions may be used containing ^*/+- as needed. No whitespace may appear in numeric expressions, now between the numeric expression and the colon.
Si prefixes should be preferred over expressions(mV instead of V/1000)
To represent ratios, a number can be a unit, e.g. “u8 filllevel in 255”, denotes that 255 is full and 0 is empty.
## Message Format
Messages sent by the device on the service channel must consist of a set of datums, wherin each datum is a data point from a certain signal, and is preceded by it's signal number.
For example. A DAQ service channel with the modifier bytes:
## u16 Voltage in mV
Might send a message consisting of a zero, indicating signal 0, followed by the two bytes of the 16 bit unsigned int, followed by the signal number and data for signal 0(if one existed), etc.

Devices may send one or many datum points in this way, and are not required to send all points.

## Introduction
WBTV5 Defines a service allowing devices to act as data acquisition units. This document defines extensions to the DAQ service as defined in WBTV5.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## Bit Arrays
A bit array is a field with type bits8, bits16,bits32, or bits64.
They are logically the same as unsigned integers, but are intended to be interpreted as packed boolean arrays.
Should the “in” keyword be used to give an interpretation to the data, the interpretation should consist of a comma separated list, containing no whitespace, giving a name to each bit in the bit array, with the first name applying to the least significant bit. Example:
## bits8 buttons in A,B,X,Y,L,R,S,s
Represents one byte, representing the values of 8 buttons, as one might find on a game controller.

When the device sends it's values, a 1 in any bit position should be used to represent True, and a 0 should be used to represent False.

## The Output Control Service
The output control service is a service used to allow a device to act as an output in the same way as the DAQ service allows devices to act as inputs.
UUID(Hex):
0xCAEDB14E0D8611E4B78578F31D5D46B0
The output control service has identical semantics to the input service, except the device listens instead of transmits on the channel.
The modifier bits are used as in the DAQ service to define a set of signals in an identical manner.
For example:

## u8 brightness
When found in the modifier bits of a Output Control Service Channel would mean the device was listening for a message on that channel containing a 8 bit
 value in signal 0, which the device would use to set the brightness of some light, presumably.

A message sent on that channel might contain:

## 0x00, 0xff
To tell the device to go to full brightness.

Or:
## 0x00, 0x00
To turn the light off.

## Introduction
# WBTV 7: Stage Light Control
Version 1 by Daniel Dunn, Public Domain/CC0
The WBTV Stage light control protocol provides a standard way to control stage lighting appliances, and a way for them to provide information about themselves using a WBTV4 Service Channel.
The general model is an array of 2**16 8 bit values, which may be set, or smoothly faded.
Each device listens to a range of values determined by it's “start code”, the first value in it's range of addresses to listen to, set in a device-specific manner such as via a special channel or with DIP switches.
Each device only needs to store info about the channels it listens to, but for efficiency, one may write to the imaginary shared space of addresses as if a single device were listening.

## The STAGE Channel
This channel is used to set and fade lighting values. Messages are a stream of commands, where each command has a command byte followed by any arguments. Devices should halt and discard the remainder upon encountering an unknown command.
The total length of a STAGE message should be under 128 bytes.
Compatible devices receiving a STAGE message should execute the commands sequentially, and ignore all values written or faded that do not overlap their range.
Devices should internally use as many bits of precision as possible for the smoothest fading.

## Commands
### 0x00 Set Values
This command directly writes to the virtual 2**16 byte space. Structure(first part at the top):
Fixed uint8 0x00	Command Code
Uint16 spos	Start Position
Uint8 valcount	Number of values to write
uint8*N data	Values to be written

Where the length of data is valcount. Any fades on any values not referenced in the command should be unaffected.

### 0x01 Fade Values
This command begins a fade from the current values to the new values over a period of time.
Structure:
Fixed uint8 0x01	command code
uint16 spos	Start Address
uint8 valcount	Number of values to write
uint8 duration	Fade duration in 48ths of a second
uint8*N data	Fade destination values

Causes valcount values starting at spos to fade from their current values to the destination values specified in data.
Any fades on any values not included in the command should continue unaffected.
Where the concept of a fade is nonsensical, such as on-off only lights, fades may be ignored.

## Introduction
The WBTV STAGE protocol defines a way of controlling lighting fixtures. This document defines an extension to the STAGE protocol allowing higher resolution control.

## Labeling
Devices that are compatible with the STAGE protocol as laid out in WBTV 7 should be labeled as supporting “WBTV STAGE”. Devices also supporting all features of this document should be labeled as supporting “WBTV STAGE 2”. STAGE 2 devices must also support all commands of WBTV 7.

## 16 bit commands
16 bit STAGE commands use the same value space array as 8 bit commands. A write or fade to channel 5 should do exactly the same thing in 16 or 8 bit mode, besides the higher resolution.

Where possible, fades between 8 bit values should be handled internally as 16 bits for maximum smoothness.

## Commands
### 0x02 16 bit Set Values
This command directly writes to the virtual 2**16 byte space. Structure(first part at the top):
Fixed uint8 0x00	Command Code
Uint16 spos	Start Position
Uint8 valcount	Number of values to write
Uint16 *N data	Values to be written

Where the length of data is valcount. Any fades on any values not referenced in the command should be unaffected.

### 0x03 16 bit Fade Values
This command begins a fade from the current values to the new values over a period of time.
Structure:
Fixed uint8 0x01	command code
uint16 spos	Start Address
uint8 valcount	Number of values to write
uint8 duration	Fade duration in 48ths of a second
uint16*N data	Fade destination values

Causes valcount values starting at spos to fade from their current values to the destination values specified in data.
Any fades on any values not included in the command should continue unaffected.
Where the concept of a fade is nonsensical, such as on-off only lights, fades may be ignored.

## Introduction
This Document defines assorted things.

## The RAND channel
The RAND channel is to be used for random numbers. Hardware RNG devices may send random bytes on this channel, but only high quality, whitened bytes such as produced by radioactive decay or diode noise.

Messages can contain 1-64 random bytes. This channel should only be used for “ready to use”, full entropy, uniformly distributed bytes.

One should obviously not use these bytes for anything important if there is a possibility of rouge devices connected to the network that might spy on bytes.
## The TZOS Channel
This channel allows a device to broadcast the time offset from UTC of any time zone. Messages should consist of the time zone name(as in “US/Pacific”, followed by a null and then the current offset from UTC(The number that, when added to UTC, would produce the time in the time zone), as a 32 bit integer.
This may optionally be followed by a 32 bit unsigned integer containing the UNIX timestamp of a future time, followed by the time offset at that time as a 32 bit integer.
## The TZRQ channel
Allows a device to request the time in a specified time zone from any device that knows it. The message is simply the name of the time zone.

A device that knows the answer may respond with a TZOS message.

## The LCTZ channel
Messages on this channel should be the name of the local time zone of the device that is sending the message, optionally followed by a NUL and then the 32 bit integer offset from UTC in seconds of that zone, which itself may optionally be followed by a 32 bit unsigned integer time in UTC and then a 32 bit integer offset that applies after that time.
## The Struct In Service:
This service allows a device to recieve data formatted as an unpadded C struct. The modifier bytes must be a valid C struct definition, which should contain comments. The struct may be named anything and should use standard typedefs(uint8_t,etc). Data sent to the device must be formatted as per the struct.
UUID:
0xDD452C900D8711E4813782F41D5D46B0
## The Struct Out Service:
Same as the struct in service, except the device sends instead of receives the struct-formatted messages.
UUID:
0xED5690880D8711E4BA3289F41D5D46B0

## The NOTE channel
This channel is used for a device to send freeform UTF8 text that is not intended to be read by a machine, such as sending copyright info or a manufacturer URL on bootup.

## The EVENT channel
This channel is used for announcing or causing events to occur. Messages must be 16 byte UUIDs representing the event.

## Introduction
This document defines several physical layer variants for WBTV.

## WBTV-A
8-N-1 Serial carried over CAN signaling levels, where a logical 1 is represented by the idle or recessive state, carried over CAT5 cable using normal RJ45 jacks.

RJ45 Pin	Function
1	CAN_H
2	CAN_L
3	Reserved
4	Reserved/POWER
5	Reserved/POWER
6	Reserved
7	GND
8	GND

Both grounds should be connected together. This provides protection against large ground offsets destroying devices.

If power is supplied, the total current on BOTH LINES combined is not to exceed 600ma, the voltage is not to exceed 32V with brief 35v transients allowed.

Devices must be fully hot pluggable, and must survive a hot plug to 32V via any amount of cable.

Devices with a “pass-through” port should pass through all pins directly unless a specific reason exists to do otherwise.

Devices must function properly with + or – 5 volts of offset between the grounds of any two communicating devices.

Any devices making use of the reserved pins for any purpose should be clearly labeled with what pins they use. Besides the use of 4 and 5 for power all use of reserved pins should be considered a site specific use.

Devices(Including those with side-specific uses of reserved pins) must sustain no damage from any combination of prolonged shorts between any pins, even with 35V power applied. Devices must also survive negative 24V applied to the CAN inputs.

Any device capable of supplying current must be current limited to 600ma to prevent fire.

Devices requiring appreciable power(More than 150mA) should not draw current from the bus and should instead use an external power supply.

Devices making use of an external power supply must connect their local ground to bus ground via a 3300 to 4700 ohm resistor with a power rating of at least one half watt.

Devices must keep input current ripple to a minimum, especially in the audio band.
## WBTV-B
One wire with a pull-up resistor of 3.3k to 100k to 3.3v, idle high, non inverted, 8-N-1, used as a wired-or bus in the manner of I2C.

Devices that externally expose a WBTV-B connection must have a reasonable level of ESD protection and protection against any combination of shorts on the WBTV-B connector pins.

Since most 5V devices will still register 3.3V logic levels, most 3.3V or 5V devices can be connected simply with a 100-220 ohm protection resistor and a schottky diode.
## WBTB-USB
Full-duplex(No CSMA) over a virtual USB COM port.
## WBTV-U
Full duplex serial over standard TTL level signaling. Should be written with the voltage used(e.g. WBTV-U(5V)) or WBTV-U5

## Introduction
This document defines a way of assigning 2 byte “Nick IDs” to devices, which may also be used as STAGE start addresses. It also defines an extension to the TIME protocol.

## The Nick ID
A nick ID is a 2 byte unsigned integer, always sent little-endian, that represents a node in a compact manner. Devices supporting nick IDs should store them in flash or EEPROM and should not change them unless explicitly commanded to or manually set.

Nick IDs are deliberately much larger than the likely number of devices on a bus for flexibility of assignment. In particular, nick IDs may also be used as STAGE start addresses, giving devices an easy standard way to set their start code via the bus.

All nick IDs below 4096 are reserved. Nick ID 0 is reserved for broadcast, Nick ID 2 is reserved for unassigned but assignable via NICKID,

Nick ID 2 is for “Unassigned and not assignable”, to be used as a placeholder for devices not supporting true nick IDs to use in contexts where a Nick ID is required.

Nick ID 3 is reserved for “Unassigned and only assignable temporarily”, for use when the device does not have writable eeprom to store addresses.

IDs 32 through 255 are reserved for devices that set their ID via manual means such as a DIP switch.

IDs between 1024 and 2048 are reserved for devices using their nick ID as a STAGE address as well, although such devices may use any address.

IDs between 2048 and 2560 should be regarded as temporary addresses. A device commanded to use an address in this range should not save it to non-volatile memory and should revert to default at next boot.

When displaying Nick IDs in user software, they should be shown as padded 4 digit hexadecimal numbers, except in the context of STAGE protocol identifiers, where they should be shown in decimal.

Devices must be designed so that overlapping Nick IDs will not cause crashes as overlapping STAGE start codes may be required for some applications.
## The MYNICK channel
This channel is used for a device to announce it's nick ID. The data is simply the devices UUID followed immediately by it's current nick ID.

Devices should send this message on power-up/first connection to the network, and when they receive a SCAN message.

## The NICKID channel
This channel is used to set the nick ID of a device. The message is simply the 16 byte UUID of the target device followed by the desired new nick ID. The device may respond with a MYNICK message announcing it's new ID.

## TIME Extension
A device may optionally append it's two-byte nick ID to the end of a TIME message, to indicate the sender and allow devices to better choose their time source.

## The RANDOM channel
This channel is like the simpler RAND channel, except messages are prefixed with the sender's Nick ID, and then 0-56 bytes of random data, which must be ready to use, uniformly distributed, ready to use, already whitened, full entropy randomness generated by a physical source.

## Introduction
This document defines a way of broadcasting navigation data via WBTV.

## The NAV channel
This channel is defined for use with terrestrial and satellite navigation receivers. All messages must have the following format:

### Latitude i32
The Latitude as tenths of millionths of degrees stored as a signed integer.
### Latitude Fine u8
The fine part latitude in billionths of degrees away from 0 relative to Latitude.
### Longitude i32
The Latitude as tenths of millionths of degrees stored as a signed integer.
### Longitude Fine u8
The fine part latitude in billionths of degrees away from 0 relative to Latitude.
### Altitude i32
The altitude relative to sea level in mm.
### 32 bit Heading
The compass heading in signed tenths of microdegrees
### 32 bit Speed
The current speed in mm per second.
### 8 Bit Satellites in View
The current number of satellites in view of the receiver.
### 16 Bit Horizontal Position Error
The current estimated position error in mm, where 2**16-1= too high to represent. Values above ~65m will not be representable.

### 16 Bit Vertical Position Error
The current estimated vertical position error in mm, where 2**16-1= too high to represent. Values above ~65m will not be representable.
### 16 Bit Timestamp
The least significant 16 bits of the count of 256ths of a second since the UNIX epoch in UTC(Leap seconds should be used)
### Optional: 16 bit Nick ID
A device may optionally end the message with it's Nick ID.
### Total Message Size
The data of this message is 31 bytes. Even after framing and arbitration, the message should not be longer than 48 bytes.

The message does not include time information beyond what is necessary for timestamping because the TIME message type should be used for time synchronization. GPS receivers should provide time information where possible.

## Introduction
This document defines a way for WBTV devices to describe what STAGE protocol features they support and what they do.

## The STGPFL channel
Messages on this channel follow a simple format comprised of the sending device's STAGE start address, followed by two reserved bytes, followed by a number of bytes where each byte indicates the type of data the device expects on one of its input channels. The first byte denotes the input mapped to its start address.

Channel types above 192 are reserved should be assumed to denote special function codes that should cause an error if not recognized.

## 192 Compression
A 192followed by two additional bytes A and B denotes B more repeats of the previous A bytes, such that 1,2,3,1,2,3 could be represented as 1,2,3,192,3,1

## 16 Bit Support flag
A 193 appearing anywhere in the channel list indicates 16 bit support for both fades and sets.

## Channel Types
The channel type codes are as follows:

1. Generic Dimming
2. Red Channel
3. Green Channel
4. Blue Channel
5. Other Color Channel
6. Blacklight channel
7. Incandescent Channel
8. Hue
9. Saturation
10. Value
11. Mode Select
12. X position
13. Y position
14. Z focus
15. Fog Control
16. Gobo Select Control
17. Gobo Rotate
18. Frequency
19. Duty Cycle
20. Air-Moving Fan
21. Water Effect
22. Pneumatic Effect
23. Motor Control
24. Rotational Position
25. Linear Position

## Introduction
This document defines a way of describing the format of a datum in a single byte.

This document also defines a friendly ASCII representation of the types, which is compatible with common shorthand notation that is used elsewhere in WBTV. For example, an unsigned 8 bit integer could be denoted as u8, wheras False would be b0-false(0 byte blob with modifier false), and an 8 bit unsigned count of hundredths would be u8-centi.

In general, specifiers for ASCII representations are listed in parenthesis in the lists. The exception is fixed-length blobs, which should always be represented in bytes(A blob that must be 64 bits long would be b8, not b64.)
## Bits 0(LSB) and 1:
The first two bits indicate the data type as follows:
Bit 0	Bit 1	Type
0	0	Blob/Other Binary (b)
1	0	Unsigned Integer (u)
0	1	Two's complement Integer (i)
1	1	IEEE Float or Other( f)

## Bits 2 and 3:
The second two bits indicate the data size as follows:
For Numeric Types(Integer, Unsigned int, IEEE Float):
Bit 2	Bit 3	Type
0	0	1 byte in length or Reserved if Float(8)
1	0	2 bytes in length (16)
0	1	4 bytes in length (32)
1	1	8 bytes in length (64)

For Blob/Other Types:
Bit 2	Bit 3	Type
0	0	0 byte in length (0)
1	0	1 bytes in length (1)
0	1	2 bytes in length (2)
1	1	Prefixed by 1 length byte (n)

## Bits 4 through 7
Bits 4 through 5 describe a modifier that may be applied to the data. For numeric types this modifier is a multiplier used to map real numbers to integers. To decode, the number should be multiplied by the number in the table.
Bit 4	Bit 5	Bit 6	Bit 7(MSB)	Multiplier
0	0	0	0	10**-15 (femto)
1	0	0	0	10**-12 (pico)
0	1	0	0	10**-9 (nano)
1	1	0	0	10**-6 (micro)
0	0	1	0	1**-3 (milli)
1	0	1	0	1 (one)
0	1	1	0	10**3 (kilo)
1	1	1	0	10**6 (mega)
0	0	0	1	2**-32 (2_32nd)
1	0	0	1	2**-16 (2_16th)
0	1	0	1	2**-8 (2_8th)
1	1	0	1	2**10 (kibi)
0	0	1	1	2**20 (mebi)
1	0	1	1	2**30 (gibi)
0	1	1	1	10*-2 (centi)

For Blob/Other types this table describes the type of data:
Bit 4	Bit 5	Bit 6	Bit 7(MSB)	Multiplier
0	0	0	0	Null (null)
1	0	0	0	0 Byte Binary False(false)
0	1	0	0	0 Byte Binary True(true)
1	1	0	0	Bit Array(bits)
0	0	1	0	Binary Data(bin)
1	0	1	0	UTF-8 or ASCII (utf8)
0	1	1	0	UUID(uuid)
1	1	1	0	Little Endian Unsigned(u)
0	0	0	1	Little Endian Signed(i)
1	0	0	1	IEEE Little Endian Float(f)

## Introduction
This document defines a a channel to be used for simple IO, Control, and configuration tasks.
## The IO Channel
This channel is Reserved for simple IO tasks. Messages on this channel must begin with the two-byte Nick ID of the sender, followed by a series of events, where each message is comprised of a 4 byte header and n data bytes, with the length of each event determined by a WBTV15 Data Format Byte.

Events can either be broadcast or targeted. A message is targeted if it comes after a Select Node in the same message, otherwise it is broadcast.

Events have a class and type allowing for device compatibility via predefined event types.

Events have a port number which is used to disambiguate events. A device might emit an event representing a temperature measurement and use the port to represent a zone. Ports should be considered equivalent to objects or sub-devices. Port 0 represents the device itself as a whole.

Broadcast events should be considered as originating FROM a port, whereas targeted messages should be considered as going TO a specific port.
## Event Format
### Byte 1
Byte 2 is the message class of the message
### Byte 2
Byte 3 is the message type of the message
### Byte 3
Byte 4 is the port identifier of the message
### Byte 4
Byte 1 is a WBTV14 Data Format byte describing the data field of the message. Devices are not required to support all number formats, however 16 and 32 bit signed whole numbers, thousandths, and millionths should be considered a baseline.
## Event Classes
Event types should be written <class>:<type> and when representing as a 16 bit integer, the class should be the MSB.

Class 0 events are reserved for basic configuration functions, class 255 events are reserved for device-specific events, all other classes are just reserved.
Devices are not required to implement any events outside of Select and Deselect.
## Class 0: Protocol/Basic
### Type 0:0: Deselect
Data must be a 0 byte blob. Causes following events in the block to be interpreted as broadcast. Normally not used as broadcast is the default.
### Type 0:1 Select
Data must be a 2 byte unsigned integer. Causes following events to be interpreted as targeted to the node with that Nick ID.
### Type 0:2 Poll
Data may be arbitrary or 0-byte None. Requests that the receiving device transmit data associated with the receiving port, for instance a measurement. Ports that are normally outputs should echo back their status.
### Type 0:3 Set Auto-ACK
Data must be 0 byte true or 0 byte false. Enables or disables acknowledgement or readback on messages relevant to the targeted port.

### Type 0:4 Set Autosend Interval
Data must be 2 byte unsigned integer in centiseconds. Configures the device to send messages relevant to the given port at a specific rate.

### Type 0:5 Save State
Save whatever portion of device state associated with the targeted port is savable as the new default.

## Introduction
Class 1 IO Events(see WBTV15) are defined as general purpose events. This document also defines additional class 0 events.

Class 2 events are for “Typed Datums” such as speed measurements or settings, temperature, etc.

Keep in mind that in general, the STAGE protocol should be used instead for controlling lights and most servo control applications.

This document spans multiple pages, unlike most other WBTV documents.

## Class 0 Events
### 0:6 Node ID
Used to set or indicate a node ID such as when a device can be configured to listen or send to another specific node. Should be acknowledged by echoing back the 0:6 message. Should generally not be saved in flash unless 0:5 save state sent.

Data must be 3 byte blob, where the first two are the u8 node number and the third is the port
### 0:7 Node and Port
Used to set or indicate a node and port, such as when a device can be configured to listen or send to another specific node. Should be acknowledged by echoing back the 0:6 message. Should generally not be saved in flash unless 0:5 save state sent. Data must be 2 byte u16 indicating the node Nick ID.

### 0:8 Error
Must be blob where the first two bytes are a u16 error code and the remainder is free text. Should be sent in response to an internal error condition or to an incorrect targeted message sent to the device. Error codes below 2^12 are reserved, with 0 indicating a generic error.

May also be sent in response to SCAN messages.

## Class 1 Events
### 1:32 Key Down
Indicates any sort of button pressed. Data must be integer representing a key. Codes lower than 2**16 are reserved. Codes shorter than 48 bits are device specific. 48 and 64 bit codes should be EUI-48 or 64s, respectively. 72 and longer should be an EUI plus a number, and 128 should be a UUID.

### 1:32 Key Up
Same semantics as key down but indicates key up instead.
### 1:33 Mouse Move
Must be a 6 byte blob containing 2 signed 16 bit integers representing X and Y counts since last update, followed by one byte indicating button status, where 0 is up and 1 is down, and the first 3 LSBs are left, middle, and right, and the rest are mouse specific. The last byte is a signed 8 bit scroll encoder counts since last movement.
### 1:34 Short Text Message
Data must be UTF8. Indicates a short message to be displayed on a small screen or notification bar. When sent directly to a device, indicates the device should display it. When broadcast, indicates that certain devices may display it along with the sender's node ID.

### 1:35 Unsecured Identity
Used to indicate the detection of a simple identity token such as an RFID tag. Data must be a blob where the first data byte indicates identity type and the rest is the identifier. 0=Generic, 1=EM4100, 192+ device specific meaning.
### 1:36 Gamepad 1 Update
Must be blob with the following format: (i8 analog1 x, i8 analog1 y, i8 analog2 x, i8 analog2 y, u8 triggerL, u8 triggerR, bits16 buttons) Button Bits(1=pressed): Left(LSB), Right, Up, Down, Stick1, Stick2, L1, L2, A, B, X, Y, Start, Back, 1, 2
## Class 2 Events
The data on these events may be any numeric type, although integers with a multiplier of 0.001 are preferred, except the kilogram, where a multiplier of 10**-6 is preferred. For brevity, event types are listed as number: name as unit

2:0 Length in Meters
2:1 Mass in Kg
2:2 Time interval in seconds
2:3 Current in amperes
2:4 Temperature in Celcius
2:5 Amount of substance in mol
2:6 Luminous Intensity in candela
2:7 Plane angle, radian
2:8 Solid angle, steradian
2:9 Angle, degree
2:10 Frequency, Hertz
2:11 Power, Watt
2:12 Charge, Columb
2:13 Potential, Volt
2:14 Capacitance, Farad
2:15 Resistance, Ohm
2:16 Flux, Weber
2:17 Flux Density, Tesla
2:18 Inductance, Henry
2:19 Luminous Flux, lumen
2:20 illuminance, lux
2:21 Area, square meter
2:22 Volume, cubic meter
2:23 Sound Intensity, db
2:24 Sound Pressure, pa
2:25 Speed, m/S
2:26 Acceleration, m/S/S
2:27 Torque, Newton/Meter
2:28 Relative Humidity, 0 to 1
2:29 Refractive Index, unitless
2:30 Luminance, nit
2:31 Flow, Liters/second
2:32 Electrical Resistance per volume, Ohm/Meter
2:33 Density, kg/m3
2:34 Electrical Permitivitt, unitls