# WBTV 1 : Publish-Subscribe for Embedded Devices
## Introduction
This page presents a simple protocol for realizing publish-subscribe messaging in small low cost embedded devices using ordinary UART(8-n-1) over any wired-AND physical layer.
The protocol can be implemented in about 3K of memory+ 70 bytes of RAM.
The protocol has no special dependence on timing of byte arrivals and does not rely on timeouts to detect a node that has failed during transmission.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## Semantics
Each message can be thought of as pushing a “message” made of “segments” to a “channel”. Both the message segments and the name of the channel are arbitrary 8 bit strings.
All channels with <=6 byte names are reserved for future standardization.
To avoid conflicts, channel names should be based on URLs or UUIDs or some other unique string, but can simply be chosen arbitrarily when global compatibility is not required.
Channels can be thought of as inputs or outputs or both of the node that “owns” the channel.
Devices can use a common prefix for all their owned channels but are not required to.
## Message Structure
Every message begins with an exclamation point, followed by the N byte channel name, then a tilde as a separator , then the data, then a 2 byte

checksum, then a closing newline(ASCII 10). All data should always be little-endian.
Should the message contain multiple segments, separate them with un-escaped tildes.
## Escaping
Should a control symbol(!, ~, or \n) need to appear in data or channel name, the backslash is used to escape it. The character following a non-escaped backslash(even another backslash) is processed as a literal character.
## Checksum
The checksum is a fletcher-256 sum, as defined by the following function :
set fast and slow to zero
then for each byte to be hashed:
increment slow by the byte mod 256
increment fast by slow mod 256

Calculated over all the bytes of the raw channel, the tilde, and the raw message, but not including the escapes or any other control characters except for the tilde. The checksum is appended to the message slow byte first, making the full message structure:
!<channel>~<message><fast><slow>\n
## CSMA
To remove the need for a bus master, we use the wired-OR Physical Layer and CSMA/CD. Before sending a message, a device must pick a random length of time, and wait until the bus has been free for that time.
Devices must also listen while transmitting, and, if they detect a collision(via the wired-or), immediately cease, wait another random period(preferably 2x the initial period) and retry.
## Introduction
# WBTV 2: Time Synchronization Protocol
Often there is a need to provide accurate time synchronization to many devices. This document defines a reserved channel for that purpose.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## The TIME Channel
The TIME channel is reserved for broadcasting messages that represent the current time, as of the leading edge of the start bit of the initial ! In the message. Messages must be timestamps conforming to the following format.
## Time Stamp Format
A time stamp contains the following fields, concatenated together, plus any optional fields which may be added, which may be specified in a later document.
### UNIX Time Stamp
This must be a 64-bit signed integer representing the number of seconds elapsed since 00:00 1 January 1970, excluding leap seconds. This is identical to the 64 bit UNIX time number.
This gives enough precision for all of recorded history until millions of years from now.

### Fractional Part
This is a 32 bit unsigned integer representing the fractional part of the current time multiplied by 2**32. Where the fractional part is unknown, 2**16 should be sent to minimize average error.
### Accuracy Estimate
This is an estimate of the accuracy, given as a 8 bit signed integer E followed by am 8 bit unsigned integer M, where the maximum error in seconds is M*(2^E).
This is an extremely simple floating point format that can only represent positive integers.
The estimate should be conservative, and should be the maximum error the sender is rated to experience across the full range of working conditions.
## Device Behavior
Devices should avoid sending time messages during leap seconds, as the time number is ambiguous. Devices should be able to be configured to send time data rather frequently, on the order of up to every several seconds, to account for devices without accurate clocks.
Devices should maintain an estimate of error for their internal clock, and should ignore messages that advertise more error than that, i.e. devices with an accurate estimate of the time should ignore broadcasts from devices with a less accurate estimate of the time.

## Introduction
# WBTV 3: Device Discovery and ID
Often it becomes neccesary to uniquely identify a device, and to enumerate devices on the bus. This document establishes rules for device IDs for WBTV devices.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## The Device UUID
Every device should, but is not required to, have a 16 byte UUID, which may conform to an official UUID standard of may simply be a random string. A devices UUID should never change, and no two devices should ever have the same UUID.
## Friendly Name
Devices should, but are not required to, be able to accept a user-assigned friendly name. The method of assigning a name should be to send a single packet to channel NAME containing the target device ID followed by the name, then the end of packet.
Names may not be longer than 24 characters, and must be valid UTF-8.
Devices should announce their names at power-up or on connection, by sending their device UUID followed by their name to the MYNAME channel.
## The STATUS channel
The channel STATUS is reserved for devices to post short status updates. All messages must be composed of the device's UUID, followed by a single byte code, followed by a UTF-8 description. STATUS messages should be used when a “heartbeat signal” is required. Status code 0 indicates “Green”, 1 is “Yellow”, and 2 is “Red”. The rest are reserved.
## The INFO channel
This channel is used by devices to transmit information about themselves to the network.
Messages must be composed of the device's UUID followed by a UUID representing the device's model number,followed by the device's(Null Terminated) Friendly Name(or an empty string), followed by any amount of freeform utf8 description.
The freeform description should contain th e actual device type and manufacturer.
## The SCAN channel
Posting an empty message to the SCAN channel allows one to scan the network for devices. All devices receiving a blank message on this channel should send any information they may have about themselves and channels they own to the network, such as their friendly name, etc.
Devices should NOT immediately send their info, but should wait a random time between 0 seconds and several tens of seconds, and should use a higher than usual backoff period and a lower priority.
Devices may also ignore SCAN and optionally provide a discover button, the pressing of which causes information to be transmitted.
Devices should only use SCAN with full knowledge that the network will be heavily trafficked from responses, and that certain devices may do nothing but handle the SCAN for tens of seconds.
## Introduction
# WBTV 4: Service Discovery
Automatic network configuration is a common requirement. Consider a wind speed sensor that sends data on a specific channel, which obviously must be different between devices to allow for multiple devices to be used. How can we know what channel a device sends on?
This document defines the concept of a WBTV Service. A WBTV Service is simply a type of service a device can provide on a channel. The wind speed sensor could be thought of as providing a “wind speed service” on the channel it sends on, and a light controller could be thought of as providing a “Light Control Service” on the channel that it listens on.
Services are identified using UUIDs, and as such anyone can define a service, and publish it formally or informally in the appropriate manner, such as online or in a user manual.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## The SERV Channel
The SERV channel is reserved for service announcements, which should be made after a device powers up, or in response to SCAN messages. and messages must obey the following format:
### Owning Device
The first 16 bytes of a SERV message must contain the UUID of the owning device which is providing the advertised service,

### Service UUID
The next 16 Bytes must be the UUID of the service being provided.
### Modifier Field
The next 8 bytes after the service UUID are generic bytes that are interpreted by the user-application in a manner defined by the specification of the service being advertised.
### Channel
The remainder of the message is the channel on which the service is provided.

## Introduction
# WBTV 5: Generic Services 1
A number of applications are very common, generic, and low level, such that many different devices will need to implement such functionality. One example would be the USB mouse. In WBTV devices it is imagined some services will be repeatedly implemented. Therfore, this document defines several official generic services, for the purpose of compatibility.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.

## WBTV-DAQ Service
This service is a channel on which a device repeatedly transmits a list of values in various formats. Typical applications would be any kind of sensor, DAQ cards with multiple input channels, etc.
The channel that provides the service is bi-directional. The device will repeatedly send it's set of measurements, and any message sent TO the device(messages must be 32-bit integers), will be interpreted as an interval at which to send in milliseconds, with 0 meaning “Do Not Send”,
The messages FROM the device are made up of several “Slots”, each of which is of one of the following types:
uint8
int8
uint16
int16
uint32
int32
float32

The message may contain any number of each, however they must appear in that order. Each of the Service Modifier Bytes represents how many of each type there are. For example, if the modifier bytes are [0,0,2,0,0,0,1,0], the message format is two 16 bit unsigned integers followed by one 32 bit float.
## Generic Configuration Service
This service allows short “configuration strings” to be transferred to and from devices.
These configuration strings are device specific, and should include a “magic number” or other means of ensuring they are correct for the device being configured.
Any message sent TO the device will be interpreted as a new configuration string, unless the message is of length 0, in which case it will be interpreted as a request for the device to send it's current configuration string.
Messages sent FROM the device are either the current configuration string, or a zero byte message indicating that the devices does not allow reading the current configuration(Such as if the configuration string contains secret data like an encryption key)
Devices using this service must use INFO broadcasts to indicate their device type.
Manufacturers should provide a configuration tool, which sends a SCAN message, finds compatible devices, allows user customization of any parameters, and reads and writes the device configuration.