# WBTV 1 : Publish-Subscribe for Embedded Devices
## Introduction
This page presents a simple protocol for realizing publish-subscribe messaging in small low cost embedded devices using ordinary UART(8-n-1) over any wired-AND physical layer.
The protocol can be implemented in about 3K of memory+ 70 bytes of RAM.
The protocol has no special dependence on timing of byte arrivals and does not rely on timeouts to detect a node that has failed during transmission.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## Semantics
Each message can be thought of as pushing a “message” made of “segments” to a “channel”. Both the message segments and the name of the channel are arbitrary 8 bit strings.
All channels with <4 byte names are reserved for future standardization.
To avoid conflicts, channel names should be based on URLs or UUIDs or some other unique string, but can simply be chosen arbitrarily when global compatibility is not required.
Channels can be thought of as inputs or outputs or both of the node that “owns” the channel.
The set of channels a node owns should not change, nor should the meanings of those channels change.
The only exception is for devices with manually configurable channel assignments.
Devices can use a common prefix for all their owned channels but are not required to.
## Message Structure
Every message begins with an exclamation point, followed by the N byte channel name, then a tilde as a separator , then the data, then a 2 byte checksum, then a closing newline(ASCII 10). All data should always be little-endian.
Should the message contain multiple segments, separate them with unescaped tildes.
## Escaping
Should a control symbol(!, ~, or \n) need to appear in data or channel name, the backslash is used to escape it. The character following a non-escaped backslash(even another backslash) is processed as a literal character.
## Checksum
The checksum is a fletcher-256 sum computed over all bytes of the channel name and the data not including control chars or escapes. To compute the sum:
set fast and slow to zero
then for each byte to be hashed:
increment slow by the byte mod 256
increment fast by slow mod 256
The slow byte is transmitted first, making the checksum [slow,fast].
## CSMA
To remove the need for a bus master, we use the wired-OR Physical Layer and CSMA/CD. Before sending a message, a device must pick a random length of time, and wait until the bus has been free for that time.
Devices must also listen while transmitting, and, if they detect a collision(via the wired-or), immediately cease, wait another random period(preferably 2x the initial period) and retry.

# WBTV 2: The META channel for WBTV

## Introduction
This page presents an extension to the base WBTV protocol allowing devices to provide information about the channels they own.
Where legally possible, I place this document and protocol into the Public Domain. Elsewhere I release this work under the Creative Commons Zero License.
## META
The META channel is a special channel that any device may transmit on for supplying metadata. All messages on META must obey the following format:
### Segment 1
The channel for which the message supplies metadata.
### Segment 2
The first segment should be the name of the device type, which must be unique among all device types including different versions of one device.
### Segment 3
The second segment should contain the unique ID of the device that owns the channel for which metadata is being announced. each device must have its own globally unique ID, which can be done in a manner similar to the unique channel names in the base spec.
In the case that the device is a prototype, or for some other reason has no ID, this segment should be blank.
### Segment 4
This segment represents the field name of the data to be transmitted on the channel. A field name is a name that describes the relation between a channel and a device, like a field of an object. A voltmeter might own a channel with the field name “volts”. Field names must only be unique within a device.
### Segment 5
This segment must contain a short string that describes the data format sent or received on the channel.
 The string can be an arbitrary unique string representing a data type intended to be recognized by the interested device, and in this case should begin with x-
This allows future standardization of more general type systems

### Segment 6
The third segment is a list of flags. Valid flags, the set of which may be extended in future protocol expansions, includes:
“i” = The device that owns this channel listens on it
“o” = The device that owns this channel transmits on it.

# WBTV2: META Segment 5
## Type Strings
A type string defines a unique data type, which may be a complex or base type, and may have an interpretation such as “kelvin” or “volts” attatched.

### Formats
The type must match one of the following patterns, optionally followed by a semicolon and then the interpretation.
Basic Type:
<type>
Array:
<basetype>[size]
Variable Array:
<basetype>[min:max]
(note that min and max are inclusive)
Tuple;
(<element1type>, <element2type>)
(Any number of tuple elements are allowed)
Array of Tuples;
(<element1type>,<element2type>)[size]
Variable Array of Tuples:
(<element1>,<element2>)[min:max]

#### Examples
 “u8:volts”
“(u8,u8);voltsAC,VoltsDC”
“(u8,u16)[8]”

### Base Types
#### Unsigned ints:
u8,u16,u32,u64
#### 2's complement ints
i8,i16,i32,i64
#### IEEE Floats
Float32, float64
#### Unicode characters
utf8
(represents one byte, not one code point)